## Slide 1: Job Aid: How to Calculate TE 705
Need 3 key numbers
  Mean
    A fact calculated from observed data points
    Will change due to:
      Recalibration
      Introduction of reagent or calibrator lot number changes
      Changes to the instrumentation
  SD
    A fact calculated from observed data points
    Certain amount of imprecision is expected; inherent with the analytical system
  True Value – target value
    Used with the mean to determine bias
    Selected from the most appropriate source or combination of sources available for the test
    Remains constant for the life of the specific lot number of QC material; it is the true value after all
    The value used in comparison with the information gained after a change has occurred to monitor the analytical system
Selecting the True Value (Target Value)
  The value published in the control’s package insert for that lot number
    Limitations
      May not be stated in insert
      May be based on insufficient data performed by manufacturer
  The value obtained from an interlaboratory comparison program
    Based on your peer group performing the same method for the test
    Limitations
      Peer group may be too small to accurately reflect a true value
      Outlier laboratories in a small peer group will statistically affect the calculations
      An interlaboratory program may not be available by the manufacturer
  Cumulative mean from your laboratory’s data when the system has been stable
    Limitations
      Difficult to correctly determine accuracy from internal sources alone
      The stable system you thought you had may actually have inherent problems and constant bias
      Even though the data has been shown to be consistent from previous results over an extended time period, you may actually be consistently wrong.
      Method validation or verification studies were never performed to evaluate accuracy